## Slide 1: Arithmetic Logic Unit
Presented by
Monem Shariar Rafi
ID: 20201058
Section:A2
Course Title: Digital Logic &
System Design Lab
Course Title: CSE-210

## Slide 2: Presented to
Shammi Akhtar
Assistant Professor
Department of Computer Science and Engineering
University of Asia Pasific

## Slide 3: What Is an ALU? An arithmetic logic unit (ALU) is a digital circuit used to perform arithmetic and logic operations
Lorem ipsum dolor sit amet, consectetur adipiscing elit
Lorem ipsum dolor sit amet, consectetur adipiscing elit
Lorem ipsum dolor sit amet, consectetur adipiscing elit

## Slide 4
How does an arithmetic logic unit work?
Typically, the ALU has direct input and output access to the processor controller,
main memory (random access memory or RAM in a personal computer) and input/output devices. Inputs and outputs flow along an electronic path that is called a bus. The input consists of an instruction word, sometimes called a machine instruction word, that contains an operation code or "opcode," one or more operands and sometimes a format code. The operation code tells the ALU what operation to perform and the operands are used in the operation.

## Slide 5: FUNCTIONS OF ALU
Arithmetic logic unit performs
Some Basic arithmetic operations
( ADDITION, SUBTRACTION etc.)
Logic operations ( OR, AND, XOR and NOT)

## Slide 6: ARITHMETIC OPERATIONS LOGICAL OPERATIONS
Transfer | Add Ai with Bi` | OR
Increment | Subtraction | XOR
Addition | Decrement | AND
Add with carry | Transfer | NOT

## Slide 7: INPUTS AND OUTPUTS OF ALU
INPUTS
Operand Inputs→ 2 4 bit numbers[ variables
A(A0, A1, A2, A3 )and B(B0, B1, B2,B3)]
Select inputs→ selects which operation will be
performed [S0, S1, S2]
Carry in→ Cin
OUTPUTS
Output→ shows result of the selected
operation [L1,L2,L3,F4]
Carry out→ Cout[L5]

## Slide 8: ARITHMETIC LOGIC UNIT with parallel adder IC#7483

## Slide 10: Transfer If A=10(decimal) =1010(in binary) And B=8(decimal) =1000(in binary) WHEN S2=S1=S0=Ci=0 Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai Yi = S0. Bi + S1.Bi’=0 Zi = S2’.Ci=0 Fi=Ai So the output is 1010
1010+1=1011
So the output is
1011
Increment
AND WHEN S2=S1=S0=0,Ci=1
Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’.
Bi’=Ai
Yi = S0. Bi + S1.Bi’=0
Zi = S2’.Ci=1
Fi=Ai+1

## Slide 11: Addition If A=1010, B=1000 WHEN S2=S1=0,S0=1,Ci=0 Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai Yi = S0. Bi + S1.Bi’=Bi Zi = S2’.Ci=0 Fi=Ai+Bi 1010+1000=10010 So the output is 10010
1010+1000=10010
10010+1=10011
So the output is
10011
Add with carry
And when S2=S1=0,S0=1,Ci=1
Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai
Yi = S0. Bi + S1.Bi’=Bi
Zi = S2’.Ci=1
Fi=Ai+Bi+1

## Slide 12: Add A with B` When S2=0,S1=1,S0=0,Ci=0 Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai Yi = S0. Bi + S1.Bi’=Bi` Zi = S2’.Ci=0 Fi=Ai+Bi` 1010+0111=10001 So the output is 10001
1010+0111=10001
10001+1=10010
So the output is
0010
Subtraction
And when S2=0,S1=1,S0=0,Ci=1
Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai
Yi = S0. Bi + S1.Bi’=Bi`
Zi = S2’.Ci=1
Fi=Ai+Bi`+1
=Ai-Bi

## Slide 13: Decrement When S2=0,S1=1,S0=1,Ci=0 Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai Yi = S0. Bi + S1.Bi’=1(1111) Zi = S2’.Ci=0 Fi=Ai+1=Ai+1111 1010+1111=11001 So the output is 1001
1010+1111=11001
11001+1=11010
So the output is
1010
Transfer
And when S2=0,S1=1,S0=1,Ci=1
Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai
Yi = S0. Bi + S1.Bi’=1=1111
Zi = S2’.Ci=1
Fi=Ai+1111+1

## Slide 14: OR When S2=1,S1=0,S0=1 Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’.Bi’ =Ai+Bi Yi = S0. Bi + S1.Bi’=0 Zi = S2’.Ci=0 Fi=Ai OR Bi=Ai+Bi 1010+1000=1010 So the output is 1010
1010 XOR
1000=0010
So the output is
0010
XOR
And when S2=1,S1=0,S0=1
Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai
Yi = S0. Bi + S1.Bi’=Bi
Zi = S2’.Ci=0
Fi=Ai XOR Bi

## Slide 15: AND When S2=1,S1=1,S0=0 Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’ = Ai + Bi` Yi = S0. Bi + S1.Bi’=Bi` Zi = S2’.Ci=0 Fi=(Ai+Bi`) XOR Bi`=AiBi 1010 AND 1000=1000 So the output is 0110.
1010 XOR 1=0101
So the output is 0101.
NOT
And when S2=1,S1=1,S0=1
Xi = Ai + S2. S1’. S0’. Bi + S2 .S1. S0’. Bi’=Ai
Yi = S0. Bi + S1.Bi’=1
Zi = S2’.Ci=0
Fi=Ai XOR 1=Ai`